## Slide 1
Four Channel Mini Wire Chamber to Study Cosmic Rays
Julián Félix
Laboratorio de partículas elementales*, Departamento de Física, División de Ciencias e Ingenierías, Campus León, Universidad de Guanajuato, México.
felix@fisica.ugto.mx
*http://laboratoriodeparticulaselementales.blogspot.mx/

## Slide 2
Resume. Multiwire proportional chamber is a conventional technique to study radiation in general, and cosmic rays in particular. To study cosmic rays, it was planned, designed, constructed, characterized, and tested a four channel mini wire chamber, based on two 3 cm X 3 cm X 0.6 cm Aluminum frames, two 3 cm X 3 cm X 0.6 cm plastic frames, two 3 cm X 3 cm X 0.3 cm Aluminum frames, two electronic planes each with two Tungsten Gold plated 1 mil diameter wires, parallel and 1 cm apart each other at 30 g stretched -each plane was 90o rotated each other in the final assemble- and two Aluminum foil window to define the gas volume; it was operated with Argon 90%-CH4 10% gas mixture at 1 atmosphere and ambient temperature (20oC in the average). It is presented technical details, results on characterization, and preliminary results on cosmic rays detection.

## Slide 3
Layout
Introduction
Design and construction
Experimental Setup
Characterization
Results
Conclusions
Acknowledgements

## Slide 4
Introduction
To detect cosmic rays, and radiation in general, there are multiwire proportional chambers, parallel plate chambers, resistive plate chambers, etc. used in high energy physics, nuclear physic, etc. to detect particles or radiation in general [1] .
with applications

## Slide 5
Here in Mexico, Universidad de Guanajuato, Guanajuato, there is the Laboratorio de Partículas Elementales, a small facility to design, construct, test, and run small ionizing particle detectors, specially, cosmic ray detectors.

## Slide 6
Another view

## Slide 7
There are many projects. One of them is related with design construction and operation of a four channel mini wire chamber to study very fast cosmic ray signals and apply cosmic rays to a broad technological areas –oil and mineral exploration, etc.- and basic science research –biology, particle physics, etc.-. But the applications are, and overall, for teaching and learning physics.

## Slide 8
Design and construction
A layout of the 4 channel mini wire chamber, performed with Sketchup.
Layout of the planned mini four wire chamber. Main components –electronic boards and Aluminum frames- are shown.

## Slide 9
This detector is based on a homemade electronic board.
Electronic boards. The basic electronic circuit is shown.
Basic electronic circuit to readout the electric signal leaved by the passage of the ionizing particle.

## Slide 10
Each electronic board was placed 90o each other, with one above and other bellow rubber 4 cm X 4 cm X 0.6 cm square, with a symmetrical 3 cm X 3 cm square hollow.
In this draw, A1, A2, B1, B2 represent the four channels. With A1 and A2 are represented one electronic board; with B1, B2 are represented the other electronic board. The 9 detection regions (Rij; i, j = 1,2,3,) are shown.

## Slide 11
This system was supported by two 4 cm X 4 cm X 0.6 cm Aluminum frames with a symmetrical 3 cm X 3 cm square hollow, one for below and one for above.
Aluminum detector Cup and Aluminum frame.
Plastic and Aluminum frames.

## Slide 12
The completed system was assembled by 4 screws 1/8 in diameter. A gas chamber was formed with this stack, with one 1/8 in input plastic elbow pipe and 1/8 in output plastic elbow pipe, to circulate, take in and take out Ar 90%+CH4 10% commercial gas.
Mini four wire chamber. The basic elements are shown.

## Slide 13
The flow of gas was regulated by a glass bubbler constructed for this purpose and operated with mineral cosmetic oil.
Gas bubbler.
Operated with mineral cosmetic oil.

## Slide 14
The analogical signal was digitalized by an additional electronic board designed and constructed for this purpose.
Four channel home made digitizer electronic board.

## Slide 15
The whole system was assembled and supported by an Aluminum base to connect electrically the four channels and readout the analogical signals, and attach the digital circuit.
This is the base for the mini four channel chamber and its electronic boards.

## Slide 16
Final assembling. Many details can be seen, especially the cross disposition of the two electronic boards, 90o one with respect to the other.
Home made mini four wire chamber is shown. Many details can be seen.

## Slide 17
The four wire channel detector, the digitalizing electronic board, the high voltage power supplier, the gas system –gas bubbler and gas container-, and one oscilloscope, or the data acquisition system were assembled to operate together.
One experimental setup. Power suppliers, multimeter, and oscilloscope. Displays on the oscilloscopes are seen.
Experimental Setup

## Slide 18
Another experimental setup.

## Slide 19
Another experimental setup. Many details are shown.

## Slide 20
The four wire channel detector, the digitalizing electronic board, and the gas bubbler were home made. High voltage power supplier is an KEITHEY 2290-2 5 kV or a Home made or a POWER DESIGNS INC. Palo Alto California Model 1570; the oscilloscope is a Tektronics TDS 1001 C-EDU, or a GW INSTEK GDS-3354; and the data acquisition system is a 32 channel Compact Rio from National Instruments (http://www.ni.com/compactrio/).
Data Acquisition system. Compact RIO from National Instruments surrounded by other instruments.

## Slide 21
The applied high voltage was between 1900 V cd-2900 V dc, for both positive and negative voltages. The gas pressure was about 3 cm of oil above atmospheric pressure. The temperature is about 20 oC. The conditions were not ideal. Some contaminants are present like the following: dust, water vapor, temperature fluctuations and electrical noise.

## Slide 22
Characterization
The four wire chamber was purged and cleaned, running Ar90%-CH410% gas, for ten hours, at 3 cm of oil above the normal atmospheric pressure. After that, the electrical tests and detections test were performed.
The four wire chamber detector was operated between 0.00 Vcd-2900 Vcd, for both, negative and positive voltages. No signals were detected between 0.0 V cd and ±1800 V cd. Signals, probably produced by cosmic rays, are detected on the four channels, starting at close ±1800 V cd.
Signals obtained with positive high voltage.

## Slide 23
Signals with negative high voltage. They are more slow compared with those from positive high voltage.
Each channel operates at different voltages and at different paces.

## Slide 24
Other display of signals, or triggers, from cosmic rays.

## Slide 25
Digital signals, with analogical signals. These signals are used to count the cosmic particles that hit the detector.
Analogical and digital signal display.

## Slide 26
Also the input signal was simulated with an oscillator, to study the efficiency of the detector, electronic damping, the possible generation of cross talk signals, and the efficiency of the discriminator.
Exponential decay, and exponential crescent, signals were injected to the four wire channel detector using a Tektronic oscillator, with frequencies between 1 Hz and 1 MHz, 1 Vpp. The detector was operated at 0.0 Vcd, during these tests.
The four wire channel detector works properly with negative and positive signals; both, digital and analogical signal electronic circuits are 100% efficient, at least inside the frequencies where it was operated, and work properly.
The electronic noise is of the order or 20 mVpp. It is from the ambient, and from the power suppliers.

## Slide 27
The discriminator trigger was fixed at 3 times the noise level, about 60 mV cd.
Attenuation factor is about 50%, the output signal is about one half of the input signal, from 1 Hz up to 1 MHz.
Cross talk signals were observed; they were eliminated with a 100 Ohms electrical resistor at the input, in series with the metallic fiber detector.

## Slide 28
Results
The amplitudes of signals are of the order of 300 mV, but are variables; they are related with the energy cosmic particles deposit on the gas chamber.
The average amplitude depends on the applied high voltage close to linearly, for both negative and positive voltages.

## Slide 29
Pulse from the mini four channel chamber compared with pulse from Z. Ahmed et al, IOP Publishing Ltd and Sissa Medialab srl. Doi: 10.1088/1748-0221/9/01/P01009.
The observed rise time is about 5 ns; the decay time, about 20 ns.
It is seen that this four wire chamber is faster than others, which makes it very convenient to study fast signals.
Pulse from Z. Ahmed et al, IOP Publishing Ltd and Sissa Medialab srl. Doi: 10.1088/1748-0221/9/01/P01009.

## Slide 30
The frequency of the number of counts versus the number of counts.
Frequency of counts Vs number of counts.

## Slide 31
Conclusions
The four wire chamber detector works properly, in spite of the no ideal conditions were it was constructed and operated.
Amplitude signals of the order of 300 mV were acquired. No electronic amplifiers were required.
It is a fast detector: rising time 5 ns; falling time 20 ns. It is good for Time of Flight studies.
The digitalizing electronic board works fine. It is possible to count events produced by the detector from cosmic particles.
Much more studies are needed, like efficiency, analogical signal amplitude dependence on detector high voltage, time resolution, space resolution, calibration.
Big detectors are made assembling and synchronizing hundreds, even millions, of small detectors, to collect and combine information from each one.

## Slide 32
Acknowledgements
CONACyT grant CONACYT, Fondo I0017 Fondo SEP - CONACYT Solicitud 000000000223179

## Slide 33
Thanks a lot