## Slide 1: Physical and experimental basis for radio therapy
Guy Paic
Instituto de Ciencias Nucleares, UNAM

## Slide 2: How does radiation interact with matter -

## Slide 3
2. Inelastic collisions
1
1
2
2
EXCITATION
2
2
1
1
IONISATION
The particle collides with the atom ic electrons:
INTERACTIÓN of PARTICLES WITH MATTER

## Slide 4
3. Radiative collision - bremstrahlung
The charged particle (electron) is deviated by the positive charge of the nucleus and emits a photon

## Slide 5
The particles lose energy in the matter
The range is the length (taken rectilinear) in the matter
range

## Slide 6
Interaction of photons with matter
ATENUATION: N = N0 e -m x
x = length
m = linear coefficient of attenuation= probability of interaction per unit of length
N
NO
Valid for
monoenergetic photons
When the electromagnetic radiation (X-rays or gammas ) enters in a natural medium the photons lose their numbers during their travel in the matter due to absorptions and dispersions

## Slide 7
Interaction of particles with matter
2. Inelastic collisions:
1
1
2
2
EXCITATION
2
2
1
1
IONISATION
The particle provoques:

## Slide 8: Interactions of Particles with Matter
The fact that particles interact with matter allows us to measure their properties, and reconstruct high energy interactions.
Dominant interaction is due to the electromagnetic force, or coulomb interactions.
Ionization and excitation of atomic electrons in matter are the most common processes.
Radiation can become important, particularly for electrons.
The nuclear interactions play a less significant role

## Slide 9: Important to understand
The Photons are losing energy in a stochastic way – that is every photon has a probability to survive after a given thickness of absorber.
Like if I have 100 dices and I decide to remove all the sixes after a throw. I will stay with a given number of dices in play after the first throw. I throw again, and again if I have many dices you can imagine that after many throws (analogous to the thickness of material I will still have dices on the table. This is called the logarithmic absorption
For charged particles the situation is different : every particle is losing energy continuously like a car without engine on a flat road: after a given path it will stop…. It means for each particle we can calculate the Range it will have in a given piece of material due to its energy, mass and charge.

## Slide 10: Most important ! The energy loss
The charged particles loose energy continuously but at a different rate:
  The slower they move the more energy they loose per unit of path!
  A the atomic number of the particle ,q the elementary charge and E is the energy of the particle

## Slide 11: Using the ionisation and/or excitation
The ionisation creates “free” electrons that can be collected
The excitation in some cases emit visible light that can be detected

## Slide 12: Ionisation plus excitation –streamer chamber

## Slide 13: Ionisation in solids – Si detectors

## Slide 14: To see the signals we need amplification

## Slide 15: Multiplying the electrons Creating an avalanche in the gas

## Slide 17: Multigap resistive plate chambers

## Slide 18: Multigap resistive plates

## Slide 19: Gas electron multipliers (GEMs)
Interesting applications: with multiple GEM foils no longer need any charge multiplication near anode. Combine GEMs with strip or pad detectors or even Silicon pixel detectors to get thin (and thus fast) particle detectors.
Thin perforated kapton foil, metal clad on both sides. (~500V)
Field lines squeezed through small gaps. This causes gas amplification in the gap.
Less gas amplification needed near the anode strips.
Invented to rescue MSGC technology.
Notes: Typical amplification GEM ~100
Considered for TESLA TPC

## Slide 20: Gem operation

## Slide 21
Ionization produced by charged particles can excite atoms and molecules in the medium to higher energy levels
The subsequent de-excitation process produces lights that can be detected and provide evidence for the traversal of the charged particles
Scintillators are the materials that can produce lights in visible part of the spectrum
Scintillation Counters

## Slide 22
Two types of scintillators
  Organic or plastic
    Tend to emit ultra-violate
    Wavelength shifters are needed to reduce attenuation
    Faster decay time (10-8s)
    More appropriate for high flux environment
  Inorganic or crystalline (NaI or CsI)
    Doped with activators that can be excited by electron-hole pairs produced by charged particles in the crystal lattice
    These dopants can then be deexcited through photon emission
    Decay time of order 10-6sec
    Used in low energy detection
Scintillation Counters

## Slide 23
The light produced by scintillators are usually too weak to see
  Photon signal needs amplification through photomultiplier tubes
    Gets the light from scintillator directly or through light guide
      Photocathode: Made of material in which valence electrons are loosely bound and are easy to cause photo-electric effect (2 – 12 cm diameter)
      Series of multiple dynodes that are made of material with relatively low work-function
        Operating at an increasing potential difference (100 – 200 V difference between dynodes
Scintillation Counters – Photo-multiplier Tube

## Slide 24: Principle of photomultiplier tubes