## Slide 1: MID FEC: plastic scintillator option (WP3)
ALICE Mexico MID meeting
April 15, 2026
Guillermo Tejeda, for the MID-Mexico electronics group

## Slide 2
Outline
Introduction (MID detector)
FEC V1
Data from Beam Test
FEC Version 2 and LpGBT
Organization
Summary

## Slide 3: MuonID Detector Plastic Scintillator Option
Assumptions:
  10 rings
  18 segments per ring
  1 chamber per segment
  40 channels per chamber
  1 SiPM per channel

## Slide 4
100cm
100cm

## Slide 5: MuonID FEC details (Version 1)
FPGA
Petiroc 2A
Trigger
Control
USB
Uplink
Downlink
Designed to test PETIROC 2A with the MID module prototype.
1 Erni connectors with 32 ch
1 ASIC Petiroc 2A designed for SiPM
1 Cyclone FPGA
Power supply regulators for FEC and SiPM
Analog and digital outputs for debugging
USB communications
Clk 40MHz
Data
Power_Reg (3.3V, 2.5V, 1.2V)
Ch14/Ch15 Test inputs
Analog and Digital Output Probes
EPCQ16
JTAG
Ext_Trigger
11 I/O
32 CH Input
Clk 12MHz

## Slide 6: FEC + PP
Communication
Power consumption
Internal trigger
External trigger
PP (reduce components)

## Slide 7: FEC + RPCs Beam Test August 2025
RPC 3 RPC 1

## Slide 8: Beam Test 2025
2 GeV/c Muons
RPCs = 7500 V
RPC1 Eff = 92.78%
RPC 1_2
RPC 1_3
RPC 1_1
RPC 1_4
RPC 3_2
RPC 3_3
RPC 3_1
RPC 3_4

## Slide 9: Beam Test 2025

## Slide 10: Beam Test 2025

## Slide 11: MuonID FEC details (Version 2)
FPGA
Trigger
Control 2
VTRx+
Uplink
Downlink
Designed to test Temporoc with the Final MID module prototype.
2 Erni connectors with 32 ch
64 ch input
1 ASIC Temporoc 3 designed for SiPM
1 FPGA CycloneVI
Power supply regulators for FEC and SiPM
Analog and digital outputs for debugging
LpGBT – VTRx
USB
Ethernet
Clk 40MHz
Data 2
Power_Reg (5V, 3.3V, 2.5V, 1.2V)
Ch14/Ch15 Test inputs
Analog and Digital Output Probes
EPCQ16
JTAG
Ext_Trigger
11 I/O
32 CH Input
Temporoc 3
(64 ch)
Trigger
Control 1
Data 1
LpGBT
USB
Ethernet
32 CH Input

## Slide 12: LpGBT V3
MuonID DB from LpGBT group
  Version 3
First PCB components for prototypes
  4 bPol12V (36 CHF)
  4 bPol2V5 (56 CHF)
  4 LpGBT (100 CHF)
  VtRX+
bPol 2.5V
bPol 12V
LpGBT
VtRX+
FMC

## Slide 13: Simulation LPGBT - FPGA
Original simulation without modifying files.
Simulation process diagram.
Downlink Frame: 64‑bit bus @ 40 MHz → Reed‑Solomon encoded → serial link at 2.56 Gbps.
Uplink Frame

## Slide 14: Simulation Uplink and Downlink
Data frame: data frame generated by the Temporoc ASIC chip, comprising a header, data per channel and a footer.
Data frame sent for use in the uplink simulation.
Simulation of the downlink by injecting a data file with the same structure as the data sent by the Temporoc
Simulation of the Slow Control transmission for LPGBT programming.

## Slide 15: Plan for LpGBT
LpGBT card
LpGBT card

## Slide 16: Simulation and test of the complete communications ALICE 3 System (1)
LpGBT card

## Slide 17: Simulation and test of the complete communications ALICE 3 System (2)
MID Electronics
DCS
LpGBT card

## Slide 18: VC707 firmware

## Slide 19: Muon ID Electronics Organization
Sinaloa
  Carlos Duarte Galvan
  Juan Manuel Mejia Camacho
  Cesar Regalado Elenes
  Juan Carlos Cabanillas
UNAM
  Enrique Patiño Salazar
  Saul Aguilar
Puebla
  Emigdio Jimenez Dominguez
  Yael Antonio Vazquez Beltrán
  Guillermo Tejeda Muñoz
  Beymar Mamani Mamani
External member
  Luis A. Pérez Moreno
  Salvador ventura
FEE
Grafic Interface
SiPM
FEC-PCB
FEC-Firmware
Communication protocols
- Bi weekly meeting.

## Slide 20: Cost approximations FEC
Pigtail Lenght : 25 cm 180 for detector 20 for spare 5 for lab use
LpGBT: 180 for detector 20 for spare 5 for lab use
VTRx+: 180 for detector 20 for spare 5 for lab use
Felix card: 3 for detector 1 for spare and lab use
bPOL2V5: 180 for detector 20 for spare 5 for lab use
bPOL12V: 180 for detector 20 for spare 5 for lab use
bPOL2V5 -> 205
2870 CHF
bPOL12V -> 205
1845 CHF
lpGBT -> 205
5125 CHF
VTRx -> 205
26650 CHF
FEC V2 costs
Temporoc 3 -> 133 KCHF
FPGA -> 82 KCHF
PCB FEC -> 20 KCHF
Components
And connectors -> 50 KCHF
Assembling -> 20 KCHF
TOTAL = 341 KCHF

## Slide 21: Summary
FEC V1 prototype completed -> SiPM and RPCs
Development of the FEC version 2 -> working on schematic and PCB
LpGBT communication protocol and VtRX+ -> working on simulation and Hardware

## Slide 22: Next activities
Capturing schematic for FEC V2
  (PCB July ∼ 2026)
Review of LpGBT and VtRx+ documentation (hardware)
Analysing data of Beam Test 2025
Continue with data taking to improve parameters configurations
LpGBT PCB -> Ok
Test Board - > Ok
Simulation -> LpGBT model OK

## Slide 23: Thank You for your attention

## Slide 24: 3D View Adapt board

## Slide 25: MID Proposal
FPGA
Petiroc 2A
2
Trigger
Control 2
VTRx+
Uplink
Downlink
Clk 40MHz
Data 2
Power_Reg (5V, 3.3V, 2.5V, 1.2V)
Ch14/Ch15 Test inputs
Analog and Digital Output Probes
EPCQ16
JTAG
Ext_Trigger
11 I/O
32 CH Input
Petiroc 2A
1
Trigger
Control 1
Data 1
LpGBT
USB
Ethernet
32 CH Input
1 x 0.5 Gb/s
CRU
ASIC 1
ASIC 1
lpGBT
1 x 0.5 Gb/s
VTRx+
CRU

## Slide 26: LpGBT DC

## Slide 27: lpGBT VTRX+ and bPol components
Pigtail Lenght : 25 cm 180 for detector 20 for spare 5 for lab use
LpGBT: 180 for detector 20 for spare 5 for lab use
VTRx+: 180 for detector 20 for spare 5 for lab use
Felix card: 3 for detector 1 for spare and lab use
bPOL2V5: 180 for detector 20 for spare 5 for lab use
bPOL12V: 180 for detector 20 for spare 5 for lab use
bPOL2V5 -> 205
2870 CHF
bPOL12V -> 205
1845 CHF
lpGBT -> 205
5125 CHF
VTRx -> 205
26650 CHF

## Slide 28: Channels Distribution (proposal)
FEC
18 FEC per ring
10 m (10 rings)
180 FECs in total
40 channels/FEC
Energy & Time measuremnt
Required 180 PigTails
3 Break Out Box
10 Optical links from Break Out Box to Felix Cards
9 Gb/s required for each MID Ring
3 Felix Card -> 24 links up to 10 Gb/s
Compatible with MWPC
MID Module
Felix Card 1
MID ring 1 to 3
Felix Card 3
MID ring 7 to 10
Felix Card 2
MID ring 4 to 6
MuonID Break Out box to Felix Card Rack
Distance from MuonID module to break out Box -> 12m
Break Out box 1
Break Out box 2
Break Out box 3

## Slide 29: MID Charge (Data from coincidence between layers, Cosmics)

## Slide 30: Using 2 PMTs for external trigger

## Slide 31: Time difference (SiPM)
CH9 & Ch16
CH9 & CH17
CH9 & CH18
CH9 & CH 20
CH9 & CH 21

## Slide 32: Beam Test 2025

## Slide 33: Beam Test 2025
2 GeV/c Muons
RPCs = 7500 V
RPC1 Eff = 92.78%

## Slide 34: Beam Test 2025
2 GeV/c Muons
RPCs = 7500 V
RPC1 Eff = 92.78%
RPC3 Eff = 21.94%

## Slide 35: Beam Test 2025