## Slide 1: An Introduction to Accelerator physics Lecture 4: Instabilities & collective effects
Rende Steerenberg, CERN, Switzerland

## Slide 2: Contents:
Single-Bunch Longitudinal Instabilities
Multi-Bunch Longitudinal Instabilities
Longitudinal Modes
Bunch Lengthening
Single-Bunch Transverse Instabilities
Possible Cures
Space Charge Effects
Questions: All you wanted to know about accelerators.
Instabilities & Collective Effects

## Slide 3: Instabilities
Until now we have only considered independent particle motion.
We call this incoherent motion.
  single particle synchrotron/betatron oscillations
  each particle moves independently of all the others
Now we have to consider what happens if all particles move in phase, coherently, in response to some excitations
Instabilities & Collective Effects
Synchrotron & betatron oscillations

## Slide 4: Instabilities, How They Arise
We cannot ignore interactions between the charged particles
They interact with each other in two ways:
  Direct Coulomb interaction
    Space charge effects
    Intra beam scattering
    Beam – beam effect in colliders
  Through their environment:
    Impedances, such as vacuum chamber, cavities, etc.
A circulating bunch induces electro magnetic fields in the vacuum chamber
  These fields act back on the particles in the same or the following bunch(es)
  Small perturbation to the bunch motion, changes the induced EM fields
  If this change amplifies the perturbation then we have an instability.
Instabilities & Collective Effects

## Slide 5: Image Currents
A circulating bunch creates an image current in vacuum chamber.
Instabilities & Collective Effects
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
bunch
vacuum chamber
induced charge
The induced image current is the same size but has the opposite sign to the bunch current.
resistor
Wall Current Monitor (WCM)
Insulator
(ceramic)

## Slide 6: Image Currents & Impedance
The vacuum chamber presents an impedance to this induced wall current (changes of shape, material etc.)
The image current combined with this impedance induces a voltage, which in turn affects the charged particles in the bunch.
Instabilities & Collective Effects
Resistive, inductive, capacitive
Real & Imaginary components
Impedance & current  voltage  electric field
Strong frequency dependence

## Slide 7: Impedance sources
Any change of cross section or material leads to a finite impedance
We can describe the vacuum chamber as a series of cavities
  Narrow band - High Q resonators - RF Cavities tuned to some harmonic of the revolution frequency
  Broad band - Low Q resonators - rest of the machine
For any cavity two frequencies are important:
   = Excitation frequency (bunch frequency)
  R= Resonant frequency of the cavity
If h  R then the induced voltage will be large and will build up with repeated passages of the bunch
Instabilities & Collective Effects

## Slide 8: Single Bunch Long. Instability
Lets consider:
  A single bunch with a revolution frequency = 
  That this bunch is not centered in the longitudinal Phase Space
  A single high-Q cavity which resonates at R (R h)
Instabilities & Collective Effects
R
Higher impedance  more
energy lost in cavity
Lower impedance  less energy lost in cavity
Cavity impedance
Real Z
Frequency
h

## Slide 9: Impedance sources
Lets start a coherent synchrotron oscillation (above transition)
  The bunch will gain and loose energy/momentum
  There will be a decrease and increase in revolution frequency
Therefore the bunch will see a changing cavity impedance
Lets consider two cases:
  First case, consider R > h
  Second case, consider R < h
Instabilities & Collective Effects

## Slide 10: Single Bunch Long. Instability
Case: R> h
Instabilities & Collective Effects
Real Z
Frequency
R
h
Higher energy  lose less energy
Lower energy  lose more energy
This is unstable
The cavity tends to increase the energy oscillations
Now retune cavity so that R< h

## Slide 11: Single Bunch Long. Instability
Case: R< h
Instabilities & Collective Effects
This is stable
This is is known as the “Robinson Instability”
To damp this instability one should retune the cavity so that R< h
Real Z
Frequency
R
h
Higher energy  lose more energy
Lower energy  lose less energy

## Slide 12: Robinson Instability
The Robinson Instability is a single bunch, dipole mode oscillation.
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time

## Slide 13: Robinson Instability
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time

## Slide 14: Robinson Instability
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
Note that the width remains unchanged

## Slide 15: Robinson Instability
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time

## Slide 16: Robinson Instability
The oscillation frequency is the synchrotron frequency.
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
Mode m = 1

## Slide 17: Higher Order Modes: m=2
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time

## Slide 18: Higher Order Modes: m=2
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
After a quarter of a synchrotron period

## Slide 19: Higher Order Modes: m=2
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
After half a synchrotron period

## Slide 20: Higher Order Modes: m=2
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
After three quarter of a synchrotron period

## Slide 21: Higher Order Modes: m=2
Instabilities & Collective Effects
Charge
density
E
phase
Longitudinal
phase space
Seen on a
WCM + scope
time
After a complete synchrotron period
The oscillation frequency is 2 times synchrotron frequency.

## Slide 22: Multi-Bunch Instabilities
What if we have more than one bunch in our accelerator ring…..?
Lets take 4 equidistant bunches A, B, C & D
The field left in the cavity by bunch A alters the coherent synchrotron motion of B, which changes field left by bunch B, which alters bunch C……to bunch D, etc…etc..
Until we get back to bunch A…..
For 4 bunches there are 4 possible modes of coupled bunch longitudinal oscillation
Instabilities & Collective Effects

## Slide 23: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
Df
0
p/2
3p/2
p
A B C D

## Slide 24: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
Df
0
p/2
3p/2
p
A B C D

## Slide 25: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
Df
0
p/2
3p/2
p
A B C D

## Slide 26: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
Df
0
p/2
3p/2
p
A B C D

## Slide 27: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D
Df

## Slide 28: Coupled Bunch Instabilities
Instabilities & Collective Effects
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D
Df

## Slide 29: Coupled Bunch Instabilities
Instabilities & Collective Effects
Df
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D

## Slide 30: Coupled Bunch Instabilities
Instabilities & Collective Effects
Df
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D

## Slide 31: Coupled Bunch Instabilities
Instabilities & Collective Effects
Df
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D

## Slide 32: Coupled Bunch Instabilities
Instabilities & Collective Effects
Df
E
phase
n=0
n=3
n=2
n=1
0
p/2
3p/2
p
A B C D

## Slide 33: Coupled Bunch Instabilities
For simplicity assume we have a single cavity which resonates at the revolution frequency
With no coherent synchrotron oscillation we have:
Instabilities & Collective Effects
A B C D
E
phase
Lets have a look at the voltage induced in a cavity by each bunch and see how this acts back on the other bunches.

## Slide 34: Coupled Bunch Instabilities
Bunch A
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase

## Slide 35: Coupled Bunch Instabilities
Bunch B
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase

## Slide 36: Coupled Bunch Instabilities
Bunch C
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase

## Slide 37: Coupled Bunch Instabilities
Bunch D
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase

## Slide 38: Coupled Bunch Instabilities
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
A & C induced voltages cancel

## Slide 39: Coupled Bunch Instabilities
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
B & D induced voltages cancel

## Slide 40: Coupled Bunch Instabilities
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
All voltages cancel  no residual effect

## Slide 41: Coupled Bunch Instability n=1
Let introduce n=1 coupled bunch oscillation mode.
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase

## Slide 42: Coupled Bunch Instability n=1
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
A & C induced voltages do not cancel

## Slide 43: Coupled Bunch Instability n=1
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
Residual voltage

## Slide 44: Coupled Bunch Instability n=1
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
This residual voltage will accelerate B
and decelerate D
This increases the oscillation amplitude

## Slide 45: Coupled Bunch Instability n=1
¼ of a synchrotron period later...
Instabilities & Collective Effects
A & C induced voltages now cancel
A B C D
E
phase
V
induced
phase

## Slide 46: Coupled Bunch Instability n=1
Instabilities & Collective Effects
B & D induced voltages do not cancel
A B C D
E
phase
V
induced
phase

## Slide 47: Coupled Bunch Instability n=1
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
This residual voltage

## Slide 48: Coupled Bunch Instability n=1
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
This residual voltage will accelerate A
and decelerate C
Again  increase of oscillation amplitude

## Slide 49: Coupled Bunch Instability n=3
Hence the n=1 mode coupled bunch oscillation is unstable
Not all modes are unstable, let’s have a look at n=3
Instabilities & Collective Effects
B & D induced voltages cancel
A B C D
E
phase
V
induced
phase

## Slide 50: Coupled Bunch Instability n=3
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
A & C induced voltages do not cancel

## Slide 51: Coupled Bunch Instability n=3
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
This residual voltage

## Slide 52: Coupled Bunch Instability n=3
Instabilities & Collective Effects
A B C D
E
phase
V
induced
phase
This residual voltage will accelerate B
and decelerate D
 decrease the oscillation amplitude

## Slide 53: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects
Turn “1”
“Mountain range display, using the WCM”

## Slide 54: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects
Add snapshot images some turns later

## Slide 55: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 56: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 57: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 58: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 59: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 60: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 61: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 62: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 63: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 64: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 65: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 66: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 67: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects

## Slide 68: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects
Which coupled bunch mode is this ?
What is the synchrotron period ?

## Slide 69: Coupled Bunch Instab. on a Scope
Instabilities & Collective Effects
One Synchrotron period
This is Mode n = 2
n=2
Df = p
E
phase

## Slide 70: Possible Cures Longitudinal Instabilities
Instabilities & Collective Effects
Single Bunch:
  Tune the RF cavities correctly in order to avoid the Robinson Instability.
  Have a phase lock system, this is a feedback on phase difference between RF and bunch.
  Have correct Longitudinal matching.
  Radiation damping (Leptons).
  Damp higher order resonant modes in cavities.
  Reduce machine impedance as much as possible.
Multi Bunch:
  Reduce machine impedance as far as possible.
  Feedback systems - correct bunch phase errors with high frequency RF system.
  Radiation damping (Leptons).
  Damp higher order resonant modes in cavities.

## Slide 71: Everything Under Control ?
Now we controlled all longitudinal instabilities, but …..
It seems that we are unable to increase peak bunch current above a certain level.
The bunch gets longer as we add more particles.
Why..?
What happens….?
Lets first look at the behaviour of a cavity resonator as we change the driving frequency.
Instabilities & Collective Effects

## Slide 72: Driving & Resonant Frequencies
The phase of the response of a resonator/cavity depends on the difference between the driving and the resonant frequencies
Instabilities & Collective Effects
h
R
Response leads excitation
h

h=R
h<R
h>R
Response lags behind excitation
Cavity
impedance
Real Z
Frequency
R
Capacitive
impedance
Inductive
impedance
Inductive
Capacitive

## Slide 73: Higher Order Modes
Cavity/Resonator driven on resonance
  h = R
  Resistive impedance
Instabilities & Collective Effects
V
t
bunch
Induced voltage
Cavity/Resonator driven above resonance
  h > R
  Capacitive impedance
V
t
bunch
Induced voltage
Response leads excitation
Cavity/Resonator driven below resonance
  h < R
  Inductive impedance
V
t
bunch
Induced voltage
Response lags behind excitation

## Slide 74: Bunch Lengthening
In general the Broad Band impedance of the machine, vacuum pipe, etc. (other than the cavities) is inductive.
Since the Broad Band impedance of the machine is predominantly inductive , the response lags behind excitation.
Instabilities & Collective Effects
V
t
bunch
Induced voltage
This induced voltage seen by the bunch over 1 turn needs to be added to the accelerating cavity voltage.
The amplitude of the induced voltage depends on the bunch intensity.

## Slide 75: Bunch Lengthening
Instabilities & Collective Effects
V
t
RF Cavity voltage
Reduces apparent RF voltage
V
t
Bunch Lengthens as
Function of bunch intensity

## Slide 76: Coherent Transverse Oscillations
The complete bunch is displaced form side to side (or up and down).
A bunch of charged particles induces a charge in the vacuum chamber.
As we have already seen this creates an image currents .
If the bunch is displaced form the center of the vacuum chamber it will drive a differential wall current.
Instabilities & Collective Effects
Bunch
Bunch current
Induced current
Differential
current
Induced
magnetic field
Vacuum chamber
This differential current leads to a magnetic field, which deflects the bunch

## Slide 77: Transverse Coupling Impedance
Instabilities & Collective Effects
Frequency spectrum of bunch current
Transverse E & B fields summed around the machine
We characterize the electromagnetic response to the bunch by a transverse coupling impedance (as for longitudinal case)
Z(exactly as Zll) is also a function of frequency
Z also has resistive, capacitive and inductive components

## Slide 78: Transverse – Longitudinal Coupling
Longitudinal instabilities are related to synchrotron oscillations.
Transverse instabilities are related to synchrotron and betatron oscillations.
Why….?….
Instabilities & Collective Effects
Particles move around the machine and execute synchrotron and betatron oscillations
If the chromaticity is non zero.
Then the changing energy, due to synchrotron oscillations will also change the betatron oscillation frequency (betatron tune, Q).

## Slide 79: Single Bunch modes
As for longitudinal oscillation there are different modes for single bunch transverse oscillations
We can observe the transverse bunch motion from the difference signal on a beam position monitor (BPM)
Instabilities & Collective Effects
Sum of charges on H or V strip lines
Difference of charges on H or V strip lines

## Slide 80: Rigid Bunch Mode
The bunch oscillates transversely as a rigid unit
On a single position sensitive pick-up we can observe the following:
Instabilities & Collective Effects
Transverse displacement
time
revolution period
Change in position/turn  betatron phase advance/turn

## Slide 81: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Lets superimpose successive turns
Transverse displacement

## Slide 82: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 83: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 84: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 85: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 86: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 87: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 88: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 89: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 90: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 91: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 92: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement

## Slide 93: Rigid Bunch Mode on a Scope
Instabilities & Collective Effects
Transverse displacement
Standing wave without node  Mode M = 0

## Slide 94: Cure for Rigid Bunch Mode
Instabilities & Collective Effects
To help avoid this instability we need a non-zero chromaticity
The bunch has an energy/momentum spread
The Particles will have a spread in betatron frequencies
A spread in betatron frequencies will mean that any coherent transverse oscillation (all particles moving together) will very quickly become incoherent again.

## Slide 95: Higher Order Bunch Modes
…
Instabilities & Collective Effects
Higher order modes are called “Head-tail” modes as the electro-magnetic fields induced by the head of the bunch excite oscillation of the tail.
However, these modes may be harder to observe as the center of gravity on the bunch may not move…..
Nevertheless, they are very important and cannot be neglected.

## Slide 96: Head-Tail Bunch Mode
Head & Tail of bunch move π out of phase with each other
Again, lets superimpose successive turns
Instabilities & Collective Effects

## Slide 97: Head-Tail Bunch Mode
Instabilities & Collective Effects

## Slide 98: Head-Tail Bunch Mode
Instabilities & Collective Effects

## Slide 99: Head-Tail Bunch Mode
Instabilities & Collective Effects

## Slide 100: Head-Tail Bunch Mode
Instabilities & Collective Effects

## Slide 101: Head-Tail Bunch Mode
Instabilities & Collective Effects

## Slide 102: Head-Tail Bunch Mode
Instabilities & Collective Effects
This is a standing wave with one node
Thus: Mode M=1

## Slide 103: Head-Tail Bunch Mode
Instabilities & Collective Effects
This is (obviously!) Mode M=2.

## Slide 104: Real Life Head-Tail Bunch Modes
Instabilities & Collective Effects
Some real life examples of higher order head-tail modes.
M=4
M=5
M=7
M=6
M=10

## Slide 105: Space Charge Effects
Instabilities & Collective Effects
Between two charged particles in a beam we have different forces:
Coulomb
repulsion
Magnetic attraction
I=ev
b
b=1
attractive
repulsive
+
+
magnetic
coulomb
force
total
force
0

## Slide 106: Space Charge Effects
Instabilities & Collective Effects
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Charges  repulsion
Parallel currents  attraction
For many particles in a beam we can represent it as following:

## Slide 107: Bunch Lengthening
Instabilities & Collective Effects
x
x
Uniform density distribution
y
linear
Defocusing force
At low energies, which means β<<1, the force is mainly repulsive  defocusing
It is zero at the centre of the beam and maximum at the edge of the beam.

## Slide 108: Space Charge Tune Shift
Instabilities & Collective Effects
Classical electron radius
Number of particles in the beam
Transverse emittance
Relativistic parameters
For the uniform beam distribution, this linear defocusing leads to a tune shift given by:
This tune shift is the same for all particles and vanishes at high momenta (β=1, γ>>1)
However in reality the beam distribution is not uniform….

## Slide 109: Space Charge Defocussing
Instabilities & Collective Effects
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
x
x
Linear
Non-linear
Defocusing force
Non-uniform density distribution (e.g. Gaussian)
y

## Slide 110: Laslett Tune Shift
Instabilities & Collective Effects
half of the uniform tune shift
For the non-uniform beam distribution, this non-linear defocusing means the ΔQ is a function of x (transverse position)
This leads to a spread of tune shift across the beam
This tune shift is called the LASLETT tune shift.
This tune spread cannot be corrected and does get very large at high intensity and low momentum

## Slide 111: Space Charge Tune Shift
Instabilities & Collective Effects
Tune Shift
At injection into the PS Booster
  E = 0.988 GeV, γ = 1.053, β = 0.313  ΔQ  0.3
For the same beam at injection into the PS
  E = 2.3826 GeV, γ = 2.475, β = 0.915  ΔQ  0.005
For the same beam at injection into the SPS
  E = 14 GeV, γ = 14.93, β = 0.998  ΔQ  0.00001
We accelerate the beam in the PSB as quickly as possible to avoid problems of blow-up due to betatron resonances
Large “neck tie”
in tune diagram

## Slide 112: Injector upgrade for HL-LHC
Instabilities & Collective Effects
LINAC4 at 160 MeV instead of 50 MeV.
PSB H- injection instead of multi-turn injection
PSB extraction and PS injection energy upgrade.
PS transverse and longitudinal damper
PS improved radiation shielding
SPS new RF cavities.
SPS carbon coating to avoid electron cloud instabilities.
Aim: produce brighter and more intense beams in the injector chain in order to produce higher luminosity in the LHC.

## Slide 113
Questions ?
Instabilities & Collective Effects