## Slide 1: An Introduction to Accelerator physics Lecture 2: Lattices & Resonances
Rende Steerenberg, CERN, Switzerland

## Slide 2: Contents:
Lattices and TWISS Parameters
Tune Calculations and Corrections
Dispersion
Momentum Compaction
Chromaticity
Sextupole Magnets
Normalized Phase Space
Dipolar, Quadrupolar and Sextupolar errors
Coupling
Tune Diagram
Lattices & Resonances

## Slide 3: Matrices and Hill’s equation
We can multiply the matrices of our drift spaces and quadrupoles together to form a transport matrix that describes a larger section of our accelerator or even a complete turn around the accelerator.
The results of this matrix calculation should then be identical to the result obtain from Hill’s equation.
Lattices & Resonances

## Slide 4: Matrices and Hill’s equation
Assume that our transport matrix describes a complete turn around the machine.
Therefore : (s2) = (s1)
Let μ be the change in betatron phase over one complete turn.
Then we get for x(s2):
Lattices & Resonances

## Slide 5: Matrices and Hill’s equation
So, for the position x at s2 we have…
Equating the sine terms gives:
Equating the cosine terms gives:
Resulting in:
These resulting in:
Repeat this for c and d and use the parameters we previously defined, which are called TWISS parameters.
and
Lattices & Resonances

## Slide 6: Lattice parameters
This matrix describes one complete turn around our machine and will vary depending on the starting point (s).
If we start at any point and multiply all of the matrices representing each element all around the machine we can calculate α, β, γ and μ for that specific point, which then will give us β(s) and Q
Where:
If we repeat this many times for many different initial positions (s) we can calculate our Lattice Parameters for all points around the machine.
Number of betatron oscillations per turn
Lattices & Resonances

## Slide 7: Matrices and Hill’s equation
Obviously μ (or Q) is not dependent on the initial position “s”, but we can calculate the change in betatron phase, dμ, from one element to the next.
Computer codes like “MAD” or “Transport” vary lengths, positions and strengths of the individual elements to obtain the desired beam dimensions or envelope β(s) and the desired Q.
Often a machine is made of many individual and identical sections (FODO cells). In that case we only calculate a single cell and not the whole machine, as the the functions β (s) and dμ will repeat themselves for each identical section.
The insertion sections have to be calculated separately
Lattices & Resonances

## Slide 8: The relationship between Q and b(s)
We also found:
, where μ = Δ over a complete turn.
This leads to:
Integrate over one complete turn
From this we can deduce:
  Increasing the focusing strength decreases the size of the beam envelope β and increases the betatron tune Q.
  Decreasing the focusing strength increases the size of the beam envelope β and decreases the betatron tune Q .
In practice we change de currents in the different focusing and defocusing quadrupole families to obtain the tune required.
Think about the mechanical gutter
Lattices & Resonances

## Slide 9: Tune Corrections
What happens if we change the focusing strength slightly?
The Twiss matrix for our FODO cell is given by:
Lattices & Resonances
Add a small QF quadrupole, with strength dK and length ds.
This will modify the FODO lattice, and add a horizontal focusing term:
The new Twiss matrix of the modified lattice with the extra focusing is:

## Slide 10: Tune Corrections
Provided d is small, we can ignore the changes in β
Lattices & Resonances
This extra quadrupole will modify the phase advance  for the FODO cell.
Therefore the new Twiss matrix is just:
1 =  + d
New phase advance
Change in phase advance

## Slide 11: Tune Corrections
Should be be equal to:
Lattices & Resonances
Therefore:
Combining and comparing the first and the fourth terms of these two matrices gives:
Only valid for change in b <<
1 =  + d and dμ is small
Therefore:

## Slide 12: Tune Corrections
Lattices & Resonances
If we follow the same reasoning for both transverse planes for both QF and QD quadrupoles we get:
Let dkF = dk for QF and dkD = dk for QD
bhF, bvF = b at QF and bhD, bvD = b at QD
QF
QD
We get:
This matrix relates the change in the tune to the change in strength of the quadrupoles.
We can invert this matrix to calculate change in quadrupole field needed for a given change in tune

## Slide 13: Dispersion
Until now we have assumed that our beam has no energy or momentum spread:
and
Different energy or momentum particles have different radii of curvature (ρ) in the main dipoles.
These particles no longer pass through the quadrupoles at the same radial position.
Quadrupoles act as dipoles for different momentum particles.
Closed orbits for different momentum particles are different.
This horizontal displacement is expressed as the dispersion function D(s)
D(s) is a function of s exactly as β(s) is a function of s
Lattices & Resonances

## Slide 14: Dispersion
The displacement due to the change in momentum at any position (s) is given by:
D(s) the dispersion function, is calculated from the lattice, and has the unit of meters.
The beam will have a finite horizontal size due to it’s momentum spread.
In the majority of the cases we have no vertical dipoles, and so D(s)=0 in the vertical plane.
Local radial displacement due to momentum spread
Dispersion function
Lattices & Resonances

## Slide 15: Momentum Compaction Factor
The change in orbit with the changing momentum means that the average length of the orbit will also depend on the beam momentum.
This is expressed as the momentum compaction factor, α p, where:
αp tells us about the change in the length of radius of the closed orbit for a change in momentum.
Lattices & Resonances

## Slide 16: Chromaticity
The focusing strength of our quadrupoles depends on the beam momentum, p.
Therefore a spread in momentum causes a spread in focusing strength
Q depends on the k of the quadrupoles
3.3356 p
The constant here is called Chromaticity
Lattices & Resonances

## Slide 17: Chromaticity Visiualized
The chromaticity relates the tune spread of the transverse motion with the momentum spread in the beam.
p0
A particle with a higher momentum as the central momentum will be deviated less in the quadrupole and will have a lower betatron tune
A particle with a lower momentum as the central momentum will be deviated more in the quadrupole and will have a higher betatron tune
Focusing quadrupole in horizontal plane
p > p0
p < p0
QF
Lattices & Resonances

## Slide 18: Chromaticity Calculated
Remember
and
The gradient seen by the particle depends on its momentum
Therefore
This term is the Chromaticity ξ
To correct this tune spread we need to increase the quadrupole focusing strength for higher momentum particles, and decrease it for lower momentum particles.
This we will obtain using a sextupole magnet
Lattices & Resonances

## Slide 19: Sextupole Magnets
Conventional Sextupole from LEP, but looks similar for other “warm” machines.
~ 1 meter long and a few hundreds of kg.
Correction Sextupole of the LHC
11cm, 10 kg, 500A at 2K for a field of 1630 T/m2
Lattices & Resonances

## Slide 20: Chromaticity Correction
The effect of the sextupole field is to increase the magnetic field of the quadrupoles for the positive x particles and decrease the field for the negative x particles.
However, the dispersion function, D(s), describes how the radial position of the particles change with momentum.
Therefore the sextupoles will alter the focusing field seen by the particles as a function of their momentum.
This we can use to compensate the natural chromaticity of the machine.
x
By
Final “corrected” By
By = Kq.x
(Quadrupole)
By = Ks.x2
(Sextupole)
Lattices & Resonances

## Slide 21: Sextupoles & Chromaticity
In a sextupole for y = 0 we have a field By = C.x2
Now calculate k the focusing gradient as we did for a quadrupole:
Using
which after differentiating gives
For k we write now
We conclude that k is no longer constant, as it depends on x.
For k we write now
and we know that
Therefore
Lattices & Resonances

## Slide 22: Chromaticity Correction
We know that the tune changes with :
Where:
and
Remember
with
If we can make this term exactly balance the natural chromaticity then we will have solved our problem.
The effect of a sextupole with length l on the particle tune Q as a function of Δp/p is given by:
Lattices & Resonances

## Slide 23: Where to put Sextupoles ?
There are two chromaticities:
  horizontal  ξh
  vertical  ξv
However, the effect of a sextupole depends on β(s), which varies around the machine
Two types of sextupoles are used to correct the chromaticity.
  One (SF) is placed near QF quadrupoles where βh is large and β v is small, this will have a large effect on ξh
  Another (SD) placed near QD quadrupoles, where βv is large and βh is small, will correct ξv
Lattices & Resonances
QF
QF
QF
QD
QD
SF
SF
SF
SD
SD
Also sextupoles should be placed where D(s) is large, in order to increase their effect, since Δk is proportional to D(s)

## Slide 24: Different Magnets and Imperfections
(Unfortunately) It is not possible to construct a perfect machine.
  Magnets can have imperfections
  The alignment in the de machine has non zero tolerance.
  Etc…
So, we have to ask ourselves:
  What will happen to the betatron oscillations due to the different field errors.
  Therefore we need to consider errors in dipoles, quadrupoles, sextupoles, etc…
We will have a look at the beam behaviour as a function of the tune Q
How is it influenced by these resonant conditions?
Lattices & Resonances

## Slide 25: Normalized Phase Space
By multiplying the y-axis by β the transverse phase space is normalized and the ellipse turns into a circle.
This is useful to visualize who resonances work under the influence of magnet imperfections.
Lattices & Resonances
bx’
x
Circle of radius
x’
x
Phase Space
Normalized Phase Space

## Slide 26: Normalized Phase Space & Betatron Tune
If we unfold a trajectory of a particle that makes one turn in our machine with a tune of Q = 3.333, we get:
Lattices & Resonances
0
2p
x
by’
y
2πq
This is the same as going 3.333 time around on the circle in phase space
The net result is 0.333 times around the circular trajectory in the normalized phase space
q is the fractional part of Q
So here Q= 3.333 and q = 0.333

## Slide 27: Classifying Resonances
After a certain number of turns around the accelerator the phase advance of the betatron oscillation is such that the oscillation repeats itself.
Lattices & Resonances
For example:
  If the phase advance per turn is 120º (2p/3) then the betatron oscillation will repeat itself after 3 turns.
  This could correspond to Q = 3.333 or 3Q = 10
  But also Q = 2.333 or 3Q = 7
The order of a resonance is defined as:
n × Q = integer
1st turn
2nd turn
3rd
turn
2πq = 2π/3
Let’s take a look at some illustrative cases and later add the mathematics.

## Slide 28: A Dipole kick
For a dipole, the deflection is independent of the position in the magnet.
Lattices & Resonances
y’b
y
Q = 2.00
1st turn
2nd turn
3rd turn
y’b
y
Q = 2.50
For Q = 2.00: Oscillation induced by the dipole kick grows on each turn and the particle is lost
(1st order resonance Q = 2).
For Q = 2.50: Oscillation is cancelled out every second turn, and therefore the particle motion is stable.

## Slide 29: A Quadrupolar kick
For a Quadrupole, the deflection is proportional to de displacement from the centre (deflection  position).
Lattices & Resonances
For Q = 2.50: Oscillation induced by the quadrupole kick grows on each turn and the particle is lost
(2nd order resonance 2Q = 5)
For Q = 2.33: Oscillation is cancelled out every third turn, and therefore the particle motion is stable.
Q = 2.50
1st turn
2nd turn
3rd turn
4th turn
Q = 2.33

## Slide 30: A Sextupolar kick
For a Sextupole, the deflection is proportional to de displacement from the centre squared (deflection  position2).
Lattices & Resonances
For Q = 2.33: Oscillation induced by the sextupole kick grows on each turn and the particle is lost
(3rd order resonance 3Q = 7)
For Q = 2.25: Oscillation is cancelled out every fourth turn, and therefore the particle motion is stable.
1st turn
2nd turn
3rd turn
4th turn
Q = 2.33
Q = 2.25
5th turn

## Slide 31: Amplitude Growth, a More Rigorous Approach
Let us try to find a mathematical expression for the amplitude growth in the case of a quadrupole error:
Lattices & Resonances
2πQ = phase angle over 1 turn = θ
Δβy’ = kick
a = old amplitude
Δa = change in amplitude
2πΔQ = change in phase
y does not change at the kick
y = a cos(θ)
In a quadrupole Δy’ = lky
So we have:
Δa = βΔy’ sin(θ) = lβ sin(θ) a k cos(θ)
Only if 2πΔQ is small
y’b
y
a
Dby’
Da
2πDQ
θ
θ

## Slide 32: Amplitude Growth
Lattices & Resonances
So we have:
a = l··sin() a·k·cos()
Each turn θ advances by 2πQ
On the nth turn θ = θ + 2nπQ
So, for q = 0.5 the phase term, 2(θ + 2nπQ) is constant:
Over many turns:
and thus:
Sin(θ)Cos(θ) = 1/2 Sin (2θ)
This term will be ‘zero’ as it decomposes in Sin and Cos terms and will give a series of + and – that cancel out in all cases where the fractional tune q ≠ 0.5

## Slide 33: Amplitude Growth for Quadrupoles
In this case the amplitude will grow continuously until the particles are lost.
Therefore we conclude as before that:
  quadrupoles excite 2nd order resonances for q=0.5
Thus for Q = 0.5, 1.5, 2.5, 3.5,…etc……
Lattices & Resonances

## Slide 34: Phase, A more Rigorous Approach
Lattices & Resonances
Each turn θ advances by 2πQ
On the nth turn θ = θ + 2nπQ
Over many turns:
zero
If we follow the same approach, but then concentrating on the phase we will find:
, which is correct for the 1st turn
Averaging over many turns:
Since:
we can rewrite this as:

## Slide 35: Stopband
Lattices & Resonances
This width is called the stopband of the resonance
, which is the expression for the change in Q due to a quadrupole.
But note that Q changes slightly on each turn
Related to Q
Max variation 0 to 2
Q has a range of values varying by:
So even if q is not exactly 0.5, it must not be too close, or at some point it will find itself at exactly 0.5 and lock on to the resonant condition.

## Slide 36: Sextupole, A more Rigorous Approach
Lattices & Resonances
We can apply the same arguments for a sextupole:
and thus
For a sextupole
We get :
Summing over many turns gives:
3rd order resonance term
1st order resonance term
Sextupole excite 1st and 3rd order resonance
q = 0
q = 0.33

## Slide 37: Octupole, A more Rigorous Approach
Lattices & Resonances
We can apply the same arguments for an octupole:
and thus
For an octupole
Octupolar errors excite 2nd and 4th order resonance and are very important for larger amplitude particles.
q = 0.5
q = 0.25
We get :
Summing over many turns gives:
 a2(cos 4(+2pnQ) + cos 2(+2pnQ))
Amplitude squared
4th order resonance term
2nd order resonance term
Can restrict dynamic aperture

## Slide 38: Resonances, a Summary
Quadrupoles excite 2nd order resonances
Sextupoles excite 1st and 3rd order resonances
Octupoles excite 2nd and 4th order resonances
This is true for small amplitude particles and low strength excitations
However, for stronger excitations sextupoles will excite higher order resonances (non-linear)
Lattices & Resonances

## Slide 39: Coupling
Coupling converts betatron motion from one plane (horizontal or vertical) into motion in the other plane.
Fields that will excite coupling are:
  Skew quadrupoles, which are normal quadrupoles, but tilted by 45º about it’s longitudinal axis.
  Solenoidal (longitudinal magnetic field)
Lattices & Resonances
N
S
N
S
Magnetic field
Like a normal quadrupole, but then tilted by 45º

## Slide 40: Coupling & Resonances
This coupling means that one can transfer oscillation energy from one transverse plane to the other.
Exactly as for linear resonances there are resonant conditions.
If we meet one of these conditions the transverse oscillation amplitude will again grow in an uncontrolled way.
Lattices & Resonances

## Slide 41: General Tune Diagram
Lattices & Resonances
Qh
Qv
2 2.25 2.5 2.75
2.33
2.66
2
2.25
2.5
2.75
Qh - Qv= 0
4Qh =11
2Qv =5
During acceleration we change the horizontal and vertical tune to a place where the beam is the least influenced by resonances.

## Slide 42: The Tune Diagram Measured
Lattices & Resonances
Move a large emittance beam around in this tune diagram and measure the beam losses, caused by resonances
Quantity of losses proportional to resonance strength
Not all resonance lines are harmful.
The challenge is to reduce and compensate these effects as much as possible and then find some point in the tune diagram where the beam is stable.

## Slide 43
Lattices & Resonances
Questions ?