## Slide 1: An Introduction to Accelerator physics Lecture 3: Longitudinal Motion & Beam Transfer
Rende Steerenberg, CERN, Switzerland

## Slide 2: Contents:
Basic Synchrotron Equations
Transition Crossing
Radio Frequency Cavity
Low & High Energy Longitudinal Motion
Acceleration
Adiabatic and Non-Adiabatic Changes
What is special about Leptons ?
Transfer Lines and Transverse Matching
Single and Multi-turn Injection
Betatron and Synchrotron Injection for Leptons
Single and Multi-turn Extraction
Longitudinal Motion & Beam Transfer

## Slide 3: Motion in Longitudinal Plane
What happens when particle momentum increases?
  particles follow longer orbit (fixed B field)
  particles travel faster (initially)
How does the revolution frequency change with the momentum ?
Longitudinal Motion & Beam Transfer
Change in orbit length
Change in velocity
But
Momentum compaction factor
Therefore:

## Slide 4: Frequency - Momentum
Longitudinal Motion & Beam Transfer
The relativity theory says
but
fixed by the lattice
varies with momentum
(E = E0)

## Slide 5: Transition:
Longitudinal Motion & Beam Transfer
Low momentum ( << 1,   1)
  The revolution frequency increases as momentum increases
High momentum (  1,  >> 1)
  The revolution frequency decreases as momentum increases
Lets look at the behaviour of a particle in a constant magnetic field.
For one particular momentum or energy we have:
This particular energy is called Transition energy

## Slide 6: The Frequency Slip Factor
Longitudinal Motion & Beam Transfer
Below transition  h = positive

We found
At transition  h = zero
Above transition  h = negative
Transition is very important in proton machines.
  A little later we will see why….
In the CERN PS machine : tr is at ~ 6 GeV/c
Transition does not exist in leptons machines, why?

## Slide 7: Radio Frequency Systems
Hadron machines:
  Accelerate / Decelerate beams
  Beam shaping
  Beam measurements
  Increase luminosity in hadron colliders
Lepton machines:
  Accelerate beams
  Compensate for energy loss due to synchrotron radiation.
Longitudinal Motion & Beam Transfer

## Slide 8: RF Cavity
To accelerate charged particles we need a longitudinal electric field.
Magnetic fields deflect particles, but do not accelerate them in absolute terms.
Longitudinal Motion & Beam Transfer
Particles
Vacuum chamber
Insulator
(ceramic)
V volts
If the voltage is DC then there is no acceleration !
  The particle will accelerate towards the gap but decelerate after the gap.
Use an Oscillating Voltage with the right Frequency

## Slide 9: Radio Frequency Cavities
Fixed frequency cavity
Longitudinal Motion & Beam Transfer
Variable frequency cavity

## Slide 10: A single particle and RF voltage
Lets see what a low energy particle does with this oscillating voltage in the cavity...
Longitudinal Motion & Beam Transfer
Set the oscillation frequency so that the period is exactly equal to one revolution period of the particle.
1st revolution period
V
time
2nd revolution period
V

## Slide 11: Add a second particle
After many turns B approaches A
B is still late in the cavity w.r.t. A
B still sees a higher voltage and is still being accelerated
Lets see what a second low energy particle, which arrives later in the cavity, does with respect to our first particle.
Longitudinal Motion & Beam Transfer
1st revolution period
V
time
~ 20th revolution period
V
A
B
A
B
B arrives late in the cavity w.r.t. A
B sees a higher voltage than A and will therefore be accelerated

## Slide 12: During Many Turns
Longitudinal Motion & Beam Transfer
1st revolution period
V
time
A
B

## Slide 13: During Many Turns
Longitudinal Motion & Beam Transfer
100st revolution period
V
time
A
B

## Slide 14: During Many Turns
Longitudinal Motion & Beam Transfer
200st revolution period
V
time
A
B

## Slide 15: During Many Turns
Longitudinal Motion & Beam Transfer
400st revolution period
V
time
A
B

## Slide 16: During Many Turns
Longitudinal Motion & Beam Transfer
500st revolution period
V
time
A
B

## Slide 17: During Many Turns
Longitudinal Motion & Beam Transfer
600st revolution period
V
time
A
B

## Slide 18: During Many Turns
Longitudinal Motion & Beam Transfer
700st revolution period
V
time
A
B

## Slide 19: During Many Turns
Longitudinal Motion & Beam Transfer
800st revolution period
V
time
A
B

## Slide 20: During Many Turns
Longitudinal Motion & Beam Transfer
900st revolution period
V
time
A
B

## Slide 21: Synchrotron Oscillations
Longitudinal Motion & Beam Transfer
Particle B has made 1 full oscillation around particle A.
The amplitude depends on the initial phase.
We call this oscillation:
900st revolution period
V
time
A
B
Exactly like the pendulum
Synchrotron Oscillation

## Slide 22: Longitudinal Phase Space
In order to be able to visualize the motion in the longitudinal plane we define the longitudinal phase space (like we did for the transverse phase space)
Longitudinal Motion & Beam Transfer
E
t (or )

## Slide 23: Phase Space Motion
Particle B oscillates around particle A
  This is synchrotron oscillation
When we plot this motion in our longitudinal phase space we get:
Longitudinal Motion & Beam Transfer
t (or )
E
higher energy
late arrival
lower energy
early arrival

## Slide 24: Phase Space Motion
Particle B oscillates around particle A
  This is synchrotron oscillation
When we plot this motion in our longitudinal phase space we get:
Longitudinal Motion & Beam Transfer
t (or )
E
higher energy
late arrival
lower energy
early arrival

## Slide 25: Phase Space Motion
Particle B oscillates around particle A
  This is synchrotron oscillation
When we plot this motion in our longitudinal phase space we get:
Longitudinal Motion & Beam Transfer
t (or )
E
higher energy
late arrival
lower energy
early arrival

## Slide 26: Phase Space Motion
Particle B oscillates around particle A
  This is synchrotron oscillation
When we plot this motion in our longitudinal phase space we get:
Longitudinal Motion & Beam Transfer
t (or )
E
higher energy
late arrival
lower energy
early arrival

## Slide 27: Stationary Bucket & Bunch
Bucket area = longitudinal Acceptance [eVs]
Bunch area = longitudinal beam emittance = .E.t/4 [eVs]
Longitudinal Motion & Beam Transfer
E
t (or )
E
t
Bunch
Bucket

## Slide 28: De-bunched – Coasting beam
The emittance of an unbunched beam is just ET eVs
  E is the energy spread [eV]
  T is the revolution time [s]
Longitudinal Motion & Beam Transfer
E
t (or )
E
T = revolution time

## Slide 29: What Happens Beyond transition
Until now we have seen how things look like below transition.
Longitudinal Motion & Beam Transfer
 = positive
Higher energy  faster orbit  higher Frev  next time particle will be earlier.
Lower energy  slower orbit  lower Frev  next time particle will be later.
What will happen above transition ?
 = negative
Higher energy  longer orbit  lower Frev  next time particle will be later.
Lower energy  shorter orbit  higher Frev  next time particle will be earlier.
Below transition we use the rising edge, beyond transition we will use the falling edge of the oscillating voltage.

## Slide 30: Motion Beyond Transition
Imagine two particles A and B, that arrive at the same time in the accelerating cavity (when Vrf = 0V)
  For A the energy is such that Frev A = Frf.
  The energy of B is higher  Frev B < Frev A
Longitudinal Motion & Beam Transfer
accelerating
time
E
RF Voltage
decelerating
A
B
V

## Slide 31: Motion Beyond Transition
Particle B arrives after A and experiences a decelerating voltage.
  The energy of B is still higher, but less  Frev B < Frev A
Longitudinal Motion & Beam Transfer
time
E
RF Voltage
accelerating
decelerating
A
B
V

## Slide 32: Motion Beyond Transition
B has now the same energy as A, but arrives still later and experiences therefore a decelerating voltage.
  Frev B = Frev A
Longitudinal Motion & Beam Transfer
time
time
E
RF Voltage
accelerating
decelerating
A
B
V

## Slide 33: Motion Beyond Transition
Particle B has now a lower energy as A, but arrives at the same time
  Frev B > Frev A
Longitudinal Motion & Beam Transfer
time
time
E
RF Voltage
accelerating
decelerating
A
B
V

## Slide 34: Motion Beyond Transition
Particle B has now a lower energy as A, but B arrives before A and experiences an accelerating voltage.
  Frev B > Frev A
Longitudinal Motion & Beam Transfer
time
time
E
RF Voltage
accelerating
decelerating
A
B
V

## Slide 35: Motion Beyond Transition
Particle B has now a higher energy as A and arrives at the same time again….
  Frev B < Frev A
Longitudinal Motion & Beam Transfer
time
time
E
RF Voltage
accelerating
decelerating
A
B
V

## Slide 36: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V
Phase w.r.t. RF voltage

Synchronous particle
RF Bucket
Bunch

## Slide 37: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 38: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 39: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 40: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 41: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 42: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 43: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V

## Slide 44: Motion in the bucket
Longitudinal Motion & Beam Transfer
E
t (or )
V
The particle now turns in the other direction w.r.t. a particle below transition.

## Slide 45: Below & Above Transition
Longitudinal Motion & Beam Transfer
Below transition
Stable, synchronous
position
E
t (or )
Above transition
E
t (or )

## Slide 46: RF & Harmonic Numbers
Until now we have applied an oscillating voltage with a frequency equal to the revolution frequency.
Longitudinal Motion & Beam Transfer
What will happen when Frf is a multiple of frev ???
Frf= Frev
Frf= h  Frev

## Slide 47: Harmonics & Buckets
Longitudinal Motion & Beam Transfer
We will have
h buckets
Frf= h  Frev
Harmonic number
Frequency of cavity voltage
1 Trev
Variable for
 < 1

## Slide 48: Synchrotron Frequency
On each turn the phase, , of a particle w.r.t. the RF waveform changes due to the synchrotron oscillations.
Longitudinal Motion & Beam Transfer
Change in revolution frequency
Harmonic number
We know that
Combining this with the above
This can be written as
Change of energy as a function of time

## Slide 49: Synchrotron Frequency
Longitudinal Motion & Beam Transfer
So, we have:
Where dE is just the energy gain or loss due to the RF system during each turn

V
Synchronous particle
dE = zero
V
t (or )
dE = V.sin

## Slide 50: Synchrotron Tune
Longitudinal Motion & Beam Transfer
If  is small then sin = 
and
This is a SHM where the synchrotron oscillation frequency is given by:
Synchrotron tune Qs

## Slide 51: Acceleration
Increase the magnetic field slightly on each turn.
The particles will follow a shorter orbit. (Frev < Fsynch)
Beyond transition, early arrival in the cavity causes a gain in energy each turn.
Longitudinal Motion & Beam Transfer

V
dE = V.sins
t (or )
We change the phase of the cavity such that the new synchronous particle is at s and therefore always sees an accelerating voltage
Vs = Vsins = V = energy gain/turn = dE

## Slide 52: Accelerating Bucket
Longitudinal Motion & Beam Transfer
s
E
t (or )
Stationary synchronous particle
accelerating synchronous particle
t (or )
Stationary RF bucket
Accelerating RF bucket
V

## Slide 53: Acceleration & acceptance
The modification of the RF bucket reduces the acceptance
The faster we accelerate (increasing sin s ) the smaller the acceptance
Faster acceleration also modifies the synchrotron tune.
For a stationary bucket (s = 0) we had:
Longitudinal Motion & Beam Transfer
For a moving bucket (s  0) this becomes:

## Slide 54: Non-Adiabatic Changes
What will happen when we increase the voltage rapidly ?
Longitudinal Motion & Beam Transfer
E
t (or )
Matched bunch

## Slide 55: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
The bunch is now mismatched w.r.t. to the bucket
It will start rotating

## Slide 56: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
The frequency of this rotation is equal to the synchrotron frequency

## Slide 57: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )

## Slide 58: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )

## Slide 59: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )

## Slide 60: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )

## Slide 61: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
If we let it rotate for long time w.r.t. the synchrotron frequency then all the particle with smear out, we call that filamentation

## Slide 62: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
Filamentation will cause an increase in longitudinal emittance (blow-up)

## Slide 63: Non-Adiabatic Changes
Longitudinal Motion & Beam Transfer
To avoid this filamentation we have to change slowly w.r.t. the synchrotron frequency.
This is called Adiabatic change.
E
t (or )
Matched bunch

## Slide 64: Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
Bunch is still matched

## Slide 65: Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
Bunch is still matched
It gets shorter and higher

## Slide 66: Adiabatic Changes
Longitudinal Motion & Beam Transfer
E
t (or )
The longitudinal emittance is conserved

## Slide 67: What is Special About Leptons
Since leptons are much lighter than hadrons they become relativistic very quickly during acceleration.
They emit electro magnetic waves, synchrotron radiation, under the influence of magnetic and electric forces at the following rates:
  Longitudinal proportional to the square of the energy (E2)
  Transverse proportional to the square of the magnetic field (B2)
Longitudinal Motion & Beam Transfer
PSR  E2 B2
In our accelerators:
  Transverse force >> Longitudinal force
  Therefore we only consider radiation due to transverse acceleration (thus magnetic forces)
Every turn the leptons will lose energy due to the synchrotron radiation, which has to be made up by the RF system.

## Slide 68: Synchrotron Motion for Leptons
Longitudinal Motion & Beam Transfer
All three particles will gain the same energy from the RF system
The blue particle will lose more energy than the red one.
This leads to a reduction in the energy spread, since u varies with E4.
The synchrotron oscillation can be described by the differential equation:
E
t (or )
Extra term for energy loss

## Slide 69: Betatron Motion for Leptons
Each photon emission reduces the transverse and longitudinal energy or momentum.
Longitudinal Motion & Beam Transfer
particle trajectory
ideal trajectory
particle
Emitted photon (dp)
total momentum (p)
momentum lost dp

## Slide 70: Making up for lost Energy
The RF system must make up for the loss in longitudinal energy dE or momentum dp.
However, the cavity only supplies energy parallel to ideal trajectory.
Longitudinal Motion & Beam Transfer
old particle trajectory
ideal trajectory
new particle trajectory
Each passage in the cavity increases only the longitudinal energy.
This leads to a direct reduction of the amplitude of the betatron oscillation.
This results in damping in both the horizontal and vertical plane.

## Slide 71: Leptons and emittances
Since leptons become very quickly relativistic, hence they emit synchrotron radiation in our accelerator mainly due to magnetic fields.
The RF system has to make up for the lost energy over every turn, resulting in a reduction of the longitudinal, horizontal and vertical emittances.
Due to several heating terms and coupling between the different planes the emittances shrink, but only to an equilibrium.
This is very useful in case of instabilities, but also when injecting leptons.
The drawback is that high energy (circular) leptons accelerators need lots of RF power.
Longitudinal Motion & Beam Transfer

## Slide 72: Beam transfer, Injection & Extraction
How to get a beam into and out of circular accelerators and storage rings.
The wide range of requirements will require different solutions:
  injection into a synchrotron from a LINAC
  transfer between two synchrotrons
  extraction to an end-user facility
  accumulation of particles, to increase intensity
  dealing with different particles
Longitudinal Motion & Beam Transfer

## Slide 73: Transfer Lines
Particles trajectories in transfer lines are treated the same way as in a circular machine, with the only difference that they pass only once.
We use:
  Dipoles to deflect particles
  Quadrupoles to focus particles transversely
This leads to betatron oscillations and functions
We can use the 2x2 matrices to describe the transverse motion of the particle
Longitudinal Motion & Beam Transfer

## Slide 74: Transfer Line Matrix
The particles trajectories in transfer lines are not closed
This means that the
  initial lattice parameters  final lattice parameters
Due to this the transfer matrix gets slightly more complicated.
Longitudinal Motion & Beam Transfer

## Slide 75: Transfer Between Accelerators
The initial phase space ellipse will be determined by the accelerator (1), from which the beam is being extracted (point A).
Then we calculate the transport matrix that describes the transport line and we calculate the final ellipse at point B.
However, machine (2) will have it’s own predetermined transverse phase space ellipse at B.
If the phase space ellipse, which arrives from the transfer line is different then.... what will happen to the beam?
Longitudinal Motion & Beam Transfer
1
2
A
B

## Slide 76: Transverse Mismatch
Longitudinal Motion & Beam Transfer
At injection
Injected beam rotates inside the new ellipse
“smear out” of phase space and emittance blow-up begins
emittance blow-up complete

## Slide 77: Single Turn Injection
With a single turn injection we inject one or more bunches into a synchrotron in a single turn. (revolution period of receiving machine)
Elements involved:
  Transfer line
  Septum magnet
  Fast kicker magnet
  Synchrotron (receiving machine)
Longitudinal Motion & Beam Transfer

## Slide 78: Single Turn Injection
Longitudinal Motion & Beam Transfer
Injection trajectory
Injection channel
Septum thickness
Minimize δ to reduce kicker strength
βs >>
βk >>
μ(s->k) =(2n+1)π/2

## Slide 79: Injection Oscillations
Longitudinal Motion & Beam Transfer
kicker
bpm1
bpm2
m
p/2
p/2
p/2
Error (d)
Displacement (x)
septum
Any residual transverse oscillation will lead to an emittance blow-up
Measurement methods, FFT analysis of one BPM signal, compare single-turn and closed orbit

## Slide 80: Beam Position Monitor (BPM)
Longitudinal Motion & Beam Transfer
A BPM works like a capacitor:
  Beam is for example formed by positive charges (protons).
  The vacuum is very good insulator.
  Then the strip lines will be charged with negative charges.
If the protons are nicely centered all strip lines contain an equal number of negative charges.
If the particle beam is displaced one strip line will contain more negative charges than the others.
Sum of charges on H or V strip lines
Difference of charges on H or V strip lines
Center of mass
position

## Slide 81: BPM in the LHC
Longitudinal Motion & Beam Transfer

## Slide 82: Reason for Multi-Turn Injection:
For hadrons the beam density at injection is either limited by space charge effects or by the injector (heavy ions...)
Usually we inject from a LINAC into a synchrotron
We cannot increase charge density, so we fill the horizontal phase space to increase injected intensity.
Elements used
  Septum
  Fast beam bumpers, made out of 3 or 4 dipoles for more flexibility, to create a local beam bump
Longitudinal Motion & Beam Transfer

## Slide 83: Contents:
Lets have a look at a real example…
Let qh = .25 (fractional tune)
Let us have a look what happens in phase space turn after turn
Longitudinal Motion & Beam Transfer

## Slide 84: Contents:
Longitudinal Motion & Beam Transfer
1
x
x’

## Slide 85: Contents:
Longitudinal Motion & Beam Transfer
1
2
x’
x

## Slide 86: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
x
x’

## Slide 87: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
x
x’

## Slide 88: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
x
x’

## Slide 89: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
x
x’

## Slide 90: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
7
x
x’

## Slide 91: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
7
8
x
x’

## Slide 92: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
7
8
9
x’

## Slide 93: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
7
8
9
10
x
x’

## Slide 94: Contents:
Longitudinal Motion & Beam Transfer
1
2
3
4
5
6
7
8
9
10
11
x
x’

## Slide 95: Contents:
Longitudinal Motion & Beam Transfer
x
x’

## Slide 96: Contents:
Longitudinal Motion & Beam Transfer
x
x’

## Slide 97: Contents:
Longitudinal Motion & Beam Transfer
x
x’

## Slide 98: Contents:
Longitudinal Motion & Beam Transfer
x
x’
Now the horizontal mechanical acceptance is completely filled and acceleration can start with high intensity.

## Slide 99: Multi-Turn vs. Charge Exchange Injection
Multi-turn injection:
  We need to control the tune Qh and the beam bump accurately
    in order to reduce losses
    in order to fill the horizontal phase space most efficiently
  We need a very thin septum
    in order to minimize the losses on subsequent turns
    in order to reduce phase space dilution.
Charge exchange injection:
  In order to strip the ions, but no to blow-up the beam to much we carefully need to consider the stripping foil requirements
  It has advantages over normal multi-turn proton injection
  Transport H- ions from the linac to the synchrotron
  Strip the H- ions to protons inside the ring acceptance
  It has advantages over normal multi-turn proton injection
Longitudinal Motion & Beam Transfer

## Slide 100: Charge Exchange Injection
Longitudinal Motion & Beam Transfer
beam bumpers
H- ions
Stripping foil
Injected protons
Circulating protons
We paint a more uniform transverse phase space density by modifying the beam bump and by and changing the steering of the injected beam
To avoid excessive foil heating and unnecessary beam blow up the injection bump is reduced to zero as soon as the injection is finished.

## Slide 101: Lepton Betatron accumulation Injection
We can apply the same fast injection as for hadrons, but use damping to our benefit.
Longitudinal Motion & Beam Transfer
xs
stored beam
injected beam
acceptance
xs
x
The oscillation, due to the position offset, will damp out and make place for another beam to inject.

## Slide 102: Lepton Synchrotron accumulation Injection
Longitudinal Motion & Beam Transfer
The oscillation, due to the energy offset, will damp out and make place for another beam to inject.
Dp < 0
Xs = D. Dp/p
f
E
      Injection 1
      Turn = N
stored beam
injected beam
E
f
Injection 2
Turn = N + 0.5Qs

## Slide 103: Single Turn Extraction
With a single turn ejection we eject one or more bunches out of a synchrotron in a single turn. (revolution period)
Elements involved:
  Extraction Bump
  Septum magnet
  Fast kicker magnet
  Synchronization
Longitudinal Motion & Beam Transfer
Ejection trajectory

## Slide 104: Non- Resonant Multi-Turn Extraction
Longitudinal Motion & Beam Transfer
x
x’
septum
beam
machine
acceptance
x
extracted beam
x
extracted beam
x’
x
extracted beam
x’
Tune q=0.25
Turn 1
Turn 2
Turn 3

## Slide 105: Non- Resonant Multi-Turn Extraction
Particularities:
  Use a thin septum, to reduce losses
  Use two septa (electro-static, magnetic)
  First septum is moveable, position and angle
  Only gives a few turns… (>>1010 particles/turn)
  Many users need <106 particles/second
For very high intensity beams the beam losses may be too important to use this method.
Hands on maintenance becomes difficult.
Longitudinal Motion & Beam Transfer

## Slide 106: Resonant Extraction
Experimental physicists would prefer a continuous flux out of our accelerator.
How to extract beam over thousands of turns ?
The idea is that few particles jump to the other side of the septum every revolution period
Resonant transverse motion makes the beam size increase
Set 3Qh = integer (third order resonance)
Use sextupoles to excite this resonance with correct phase.
Use a horizontal beam bump at the extraction septum, to ensure that the septum is the aperture limitation
Longitudinal Motion & Beam Transfer

## Slide 107: Resonant Extraction
This resonant extraction can generate beam spills ranging from several milliseconds up to several hours.
Longitudinal Motion & Beam Transfer
septum

## Slide 108
Questions ?
Longitudinal Motion & Beam Transfer