## Slide 1: LS1: some more work for detector and ACC experts
FSM
  SOR/EOR
  SAFE/SUPERSAFE
Dist
Web screenshots
Safety data
Alerts
Instructions
INTEGRATION

## Slide 2: FULL/FAST SOR/EOR
FULL SOR/EOR is the actual one, used during Run1
  SOR is accepted in READY (and some other states)
  EOR is accepted in all FSM states
FAST SOR/EOR is being introduced in ECS for Run2
  ECS+DCS agreed to implement it introducing a parameter in the actual SOR/EOR command instead of a new command
SOR(RUN_TYPE, RUN_NO, …, SOR_MODE)
  SOR_MODE = [FAST, FULL]
EOR (RUN_TYPE, RUN_NO, EOR_MODE)
  EOR_MODE = [FAST, FULL, COMPLETE_FAST]

## Slide 3: Renewing the FSM for ALICE RUN2 operations
ALICE will move between READY, SAFE and SUPERSAFE conditions
READY
SAFE
SUPERSAFE
ERROR
MOVING_SAFE
MOVING_SSAFE
MOVING_READY
FSM during Run1
ALICE FSM for Run2

## Slide 4: New FSM including SAFE concept
ALI_DCS
EMC_DCS
ACO_DCS
Gas
LV
HV
HV
RUN
RUN
HV
LV
RunUnit
Gas
HV
RunUnit
Run1 version
Run2 version
SAFE
SafeUnit
CU unchanged
CU new or modified
new DU

## Slide 5: Changes on the top node
READY
BEAM_TUNING
STBY_CONF
STANDBY
MOVING_...
MIXED
DET top node
GO_SAFE
ERROR
Run1: RESTORE_SAFE, RESTORE_READY were translated on the ALICE side as FSM commands (GO_BEAM_TUN, …)
DET_DCS
All states shall accept commands GO_SAFE GO_SUPERSAFE. These commands can be simply translated or sent to the DET_SAFE_CU
The FSM states of the TOP NODE don’t change
Run2: RESTORE_SAFE, RESTORE_READY are translated in the TOP NODE as FSM commands (GO_BEAM_TUN, …)
Presented at DCS workshop 18/3/2013

## Slide 6: (FIRE) SAFETY datapoint
Script and datapoint to publish safety related info for the firebrigade: AliFireSafety:
    det.isOnHV (bool)
    det.isOnLV (bool)
    det.avgTemp (float)
    det.refTemp (float)
New DpType
Example: new dp for ACO
aco_dcs:acoFireSafety.isOnHV
aco_dcs:acoFireSafety.isOnHL
aco_dcs:acoFireSafety.avgTemp
aco_dcs:acoFireSafety.refTemp
New dp
DPL file available in Z:\Install\ALICE Framework\ALICE FW Components\aliFireSafety

## Slide 7: Panels screenshots for the web
Web monitoring
  at present, the screenshots are produced centrally using a script to open the panels found in the shared area in a background UI
  each panel must stay open for several seconds to load all data
  The script producing panels screenshots shall run in the detector projects, and save PNGs in the FS shared area
Package and instructions ready and available in
Z:\Install\ALICE Framework\ALICE FW Components\aliScreenshot